## Slide 1: New project
+ = ???
Unique locomotion – two modes
Robot that can walk and fly would be useful
Drive and fly is easy, walk and fly has benefits

## Slide 2: Methodology, steps, goal
Methodology:
  Use popular RL libraries: MuJoCo, Brax, Gymnasium, Stable Baselines
  Train on GPU for vastly more training (500x+ faster, 2000+ in parallel)
Steps:
  Build custom model (CAD)
  Setup model for simulation
  Train in batches while tuning hyperparams, architecture, policy, etc.
  Optimize for natural looking and reasonably fast gait
Goal / success definition:
  Sim a pterosaur model walking with a reasonable-looking gait
  Eventually (long after this class): build robot, get it walking, then train it to fly!

## Slide 3: Model, URDF, MJCF
Got familiar with RL libraries through examples (MuJoCo, Gymnasium, Stable Baselines)
Modified example code: python and MJCF
 
+ meshes

## Slide 4: Training: Local (CPU)
Defined reward function
Set starting pose
Got more familiar with toolchain
Train!
..very slow training, no noticeable progress. Kinda just flopping around

## Slide 5: Minimal training: break dancing

## Slide 6: Training: Cloud (GPU)
GPU parallelization enables vastly faster training
Required library swaps because a lot of RL is still on CPU
Developed scripts to interpret policy and training (save all training data)
After WAY more training than on CPU, still no progress
Adjusted hyperparams:
  Reward weights
  Reward types
  Restricted some joint motion (wrist)
  Weakened actuators

## Slide 7: Some training: Yoga!!

## Slide 8: Training analysis

## Slide 9: Training analysis
https://synapsomorphy.com/filehost/train2.html
https://synapsomorphy.com/filehost/train6.html
https://synapsomorphy.com/filehost/train7.html

## Slide 10: Next steps
Continue tweaking reward
Continue restricting joint motion
More timesteps of training, especially if reward curves are promising
If walking soon: Evaluate different policies (Current: PPO)
Change mesh (potential for large speedup)